## Slide 1: Pratical Project Robotic hand grasping and lifting objects
Group: 5
Supervisor: Abdeldjallil Naceri
Tutor: Zhelin Yang
16.07.2024

## Slide 2: Agenda
1. Robotic Hands and Scenes
  Wonik - Allegro Hand
  Medium Wrap
2. PID Position Control
3. Impedance Control
4. Challenge
5. Literature sources

## Slide 3: Robotic Hands
Wonik - Allegro Hand
Multiple degrees of freedom
  4 fingers, each with 4 joints, 16 DOF
Fully driven by high precision servo motors
Integrated Sensors
allegro right hand

## Slide 4: Grasp methods and objects
Grasping objects
1.3 kg cylinder
Grasping mode
  Medium wrap
Contact model
  Hard finger contact
Scenes of gripping tasks with uncontrolled hand

## Slide 5: PID Position Control
Process of grasping and lifting by PID position controller
Predefined target joint angles
Predefined joint angles
Finger grip
Lifting

## Slide 6: Analysis of real-time position and torque
Large gap between target and actual joint angles for preset joint angles
High torque fluctuations - well outside the -4 to 4 joint torque range
What if the object is an expensive glass?

## Slide 7: Impedance Control (Torque-Based)
Process of grasping and lifting by Impedance controller
Stiffness,Ks
  Strength of control system response to position error
​Damping,B
Strength of control system response to speed errors
Mass,M
  Modelling the inertia of the system

## Slide 8: Analysis of real-time position and torque
Small and smooth fluctuations in joint position
Flexibility and stability of torque

## Slide 9: Challenge
Optimising control algorithms
Adding industrial robot forearms
Perform different types of grasping tasks through reinforcement learning

## Slide 10: Thank you for your attention.

## Slide 11: Literature sources
T. Feix, I. M. Bullock and A. M. Dollar, "Analysis of Human Grasping Behavior: Object Characteristics and Grasp Type," in IEEE Transactions on Haptics, vol. 7, no. 3, pp. 311-323, 1 July-Sept. 2014, doi: 10.1109/TOH.2014.2326871.
A. Naceri et al., "Tactile Robotic Telemedicine for Safe Remote Diagnostics in Times of Corona: System Design, Feasibility and Usability Study," in IEEE Robotics and Automation Letters, vol. 7, no. 4, pp. 10296-10303, Oct. 2022, doi: 10.1109/LRA.2022.3191563.
https://mujoco.readthedocs.io/en/stable/overview.html
GitHub - google-deepmind/mujoco_menagerie: A collection of high-quality models for the MuJoCo physics engine, curated by Google DeepMind.